## Slide 1
How We Built a Qwen 3.5/3.6 Inference Engine
Native Crystal + Metal runtime for Qwen GGUF models
30-minute technical story · simple level
Goal: understand, control, and optimize inference
Reference point: llama.cpp
Method: implement → measure → refute → keep what survives
Build → Measure → Refute
Keep only what survives
Qwen 3.5/3.6 inference engine · 01

## Slide 2
The Simple Mental Model
LLM inference is repeated matrix math plus state updates
Text becomes tokens; tokens become vectors
Each layer transforms vectors and updates memory
The final vector predicts the next token
Repeat until generation is complete
Text
Tokens
Vectors
Layers + State
Next token
Qwen 3.5/3.6 inference engine · 02

## Slide 3
Why Qwen 3.5/3.6 Was Hard
It is a hybrid model, not just a plain transformer
Full-attention layers use KV cache
Recurrent DeltaNet-style layers keep compact state
Large FFN gate/up/down projections dominate traffic
GGUF quantization: Q4_K, Q5_K, Q6_K, Q8_0
Qwen 3.5/3.6 inference engine · 03

## Slide 4
Engine Architecture
Crystal controls the graph; Metal runs the hot math
CLI, probes, benchmark harnesses
CPU/reference path for truth and debugging
Metal kernels for matmul, attention, DeltaNet, top1, state copy
CLI / probes / benchmarks
Crystal reference + scheduler
Metal kernels
Qwen 3.5/3.6 inference engine · 04

## Slide 5
Correctness Before Speed
One wrong token can change the whole continuation
Layer-level and vector checks
Logit/top1 comparisons
Greedy token parity
Approximate routes stay opt-in or proposal-only
Exact verifier decides final tokens
Qwen 3.5/3.6 inference engine · 05

## Slide 6
Prefill ≠ Decode
The same model has two very different workloads
Prefill
Many known prompt tokens Batch GEMM + chunking Throughput-oriented
Decode
One new token at a time GEMV + low latency Synchronization-sensitive
Prefill wants batch GEMM and chunking
Decode wants low latency and fewer synchronizations
Qwen 3.5/3.6 inference engine · 06

## Slide 7
Prefill: What Worked
Move from token-by-token to GPU-resident chunks
Chunked recurrent prefill on Metal
Q4/Q5/Q6 batch GEMM for prompt tokens
Skip unnecessary final-output work
Keep consecutive recurrent layers on GPU
Use attribution to find hot tensor shapes
~52.9 tok/s
early pp64
~358 tok/s
after chunking + batching
~450 tok/s
prepared-state checkpoint
Qwen 3.5/3.6 inference engine · 07

## Slide 8
Decode: What Worked
Hide overhead and avoid unnecessary work per token
Wave scheduling groups layer work
Fused greedy top1 avoids full logits when possible
Small exact fusions remove extra kernels
State preparation avoids first-touch latency
N-gram/speculative paths help on matching workloads
+4–5%
local decode snapshots vs llama.cpp
~9–14 ms/tok
repeat-heavy n-gram/spec routes
exact
verifier-gated output
Qwen 3.5/3.6 inference engine · 08

## Slide 9
Speculative Decoding
Draft fast, verify exactly
Draft proposes several tokens
Exact target verifies the chunk
Accept full prefix when it matches
On mismatch: correct one token and continue
Draft
Candidates
Exact verifier
Accept / Correct
Final output remains exact because the target model verifies the accepted tokens.
Qwen 3.5/3.6 inference engine · 09

## Slide 10
Mathematical Shortcuts
Do less proposal work, but keep exact verification
Projected-K / low-rank DeltaNet state
PCA-updown and block surrogate ideas
MTP / multi-token prediction experiments
Raw-Q8 CUDA/DP4A as proposal-only until verified
Qwen 3.5/3.6 inference engine · 10

## Slide 11
The Workflow Was The Product
Structured skepticism kept us from chasing noise
Landmark log: wins, failures, assumptions
Paired A/B instead of one-off timings
Compare against llama.cpp on same workload
Record refutations to avoid loops
Optimize after attribution names the wall
Qwen 3.5/3.6 inference engine · 11

## Slide 12
Useful Refutations
A failed experiment is progress if it narrows the search
Microbench wins sometimes regressed full prefill
Some fusions saved dispatches but hurt occupancy
CPU draft lost to sync + body cost
Fast full-row verifier could flip close logits
GPU n-gram lookup was not the wall yet
Qwen 3.5/3.6 inference engine · 12

## Slide 13
Where We Stand
Mixed status, honest claims
llama.cpp remains a strong baseline
Native decode has matched or beaten local snapshots
First-run prefill is close and measurement-sensitive
Prompt-cache and n-gram routes can win on right workloads
vLLM/MLX teach scheduler and graph-boundary lessons
Qwen 3.5/3.6 inference engine · 13

## Slide 14
Next Frontier
Turn observability into the next speed step
Quiet paired operator timing vs llama.cpp Metal
Focus hot Q4_K 4096×12288 and recurrent Q5/Q6 shapes
Continue exact n-gram/router policy work
Keep approximate routes proposal-only until verified
Qwen 3.5/3.6 inference engine · 14

## Slide 15
Takeaways
Five lessons from building the engine
1
Correctness gates first; speed second
2
Prefill and decode are different products
3
Data movement often dominates arithmetic
4
Speculation helps only when economics line up
5
A refutation log is an engineering asset
Qwen 3.5/3.6 inference engine · 15